The role of Cladophora spp and Spirulina platensis in the removal of microbial Nile water

*Osman, G. A., **Ali, M. S., *Kamel, M. M. and***Amber, A. Gad

*Bacteriology Lab., Water Pollution Research Department,**Agriculture Microbiology Department, ***Natural and Microbial products Department, National Research Center, Dokki, Cairo, Egypt.

Corresponding author, Osman, G. A., E-mail: gamalosmanali2005@yahoo.com

Abstract: The main aim of this study was to evaluate the removal of some microbial in Nile water passed through some algae (Cladophora sp and Spirulina platensis) as filters before the chlorine treatment. The other target from this filtration were to reduce the organic matter which product carcinogenic compound when exposed to the chlorine as well as reduction the chlorine doses used in Water Treatment Plants for potable water. The results show that Cladophora spp succeeded in removing  microbial tested, however, the ratio removals were 12.7, 21.1, 33.3, 11.1, 32.1, 27.2, 27.6 30.8 34.4 and 33.3% for total viable bacterial count at 37 oC, 22 oC, total coliform, fecal coliform, fecal streptococci, salmonellae group, Pseudomonas spp., total staphylococci, yeasts and fungus, respectively. On the other hand, the total organic carbons (TOC) were 9 before filtration, while after filtration was 7.5 ppm, but Spirulina platensis made reduction from 9 to 6.25 ppm. In addition, the microbial tested in Nile water samples were absent after filtrated with chlorine dose 2ppm for 30 minutes while in case Nile water samples without filtrated some microbial were present with dose 5ppm. Spirulina platensis was more efficiency where the results show that the ratio removals were 42.3, 51.5, 77.1, 80.6, 75, 45.5, 62.1, 92.3, 56.3 and 50% for total viable bacterial count at 37oC, 22oC, total coliform, fecal coliform, fecal streptococci, salmonellae group, Pseudomonas spp., total staphylococci, yeasts and fungus, respectively. After filtrated the Nile water through Spirulina platensis and treated with chlorine (dose 2ppm) for10 minutes, the microbial tested were absent while the water sample (without filtrated), some microbial were present for 60 minutes with dose 5ppm. These treatments concluded that reduction of chlorine used and carcinogenic compound in drinking water treatments as will as water quality.

[Osman, G. A., Ali, M. S., Kamel, M. M. and Amber, A. Gad. The role of Cladophora spp and Spirulina platensis in the removal of microbial Nile water. Journal of American Science 2011;7(1):784-790]. (ISSN: 1545-1003). http://www.americanscience.org.

Key words: Nile water, Classical bacterial indicators, Salmonellae group, Total staphylococci, Pseudomonas spp. yeasts, fungus, and chlorine.

Introduction

Material and methods

● Sample collection

Nile water samples were collected at inlet of El-Giza Water Treatment plant. It collected in 10 liters sterile glass bottles (10 bottles) and then transferred from the sites to the lab in ice box. The water was putting in sterile container (150 litters) and transfer by motor with flow rate 2  liters / minute to the system figure (1). Water sampling was taken at 0, 10, 30, 60 and 120 minutes in 1 liter sterile glass bottles. Sodium thiosulphate crystals (18 mg/L) were added only to the bottles samples of chlorinated drinking water (APHA, 2005).

● Chlorine water

Chlorine water was prepared from the lab of El-Giza Water Treatment plant. It added to the Nile water and filtrated water with doses 2 ppm and 5ppm, respectively according to APHA, 2005.

● Estimated the total organic carbons (TOC) and carcinogenic materials

The total organic carbons (TOC) and carcinogenic materials were estimated in water samples according to APHA, 2005.

● Microbiological examination

Enumeration of Classical bacterial indicators: Total bacterial counts (at 22ºC and 37ºC), total coliform, facal coliform and facal streptococci were carried out using poured plate and MPN methods according to APHA (2005), for raw water and drinking water.

Detection and enumeration of Pseudomonas aeruginosa was using asparagine broth media as a presumptive test (MPN methods for raw water and drinking water according to APHA, 2005). The positive tubes produced a greenish fluorescent color after exposing to long-wave ultraviolet light. These tubes were used to streak the surface of acetamide agar slants as confirmation test. Positive confirmed tubes with the purple color indicated to high pH value after incubated at 37ºC for 24 hours (APHA, 2005).

Detection and enumeration of salmonellae group were carried out using membrane filter technique. A 100 ml drinking water samples were separately filtrated through the membrane filter (0.45 μm pore size and 47 mm diameter). The membrane was transferred onto bismuth sulphate agar as a confirmed test. (APHA, 2005). On the other hand, for Nile water samples (ml samples), salmonellae groups was counted from inoculated     5ml autoclaving buffer peptone water (British Standard Institute, 2002) tubes (incubated at 37ºC for 24 hours) which used as MPN technique. 0.2 ml from these tubes was streaked (by rod glass) on the plates of bismuth sulphate agar as a confirmed test. After incubation at 37ºC for 48 hours, typical black colonies with or without metallic sheen and blackening extended beyond the colonies considered as confirmed positive results for the presence of salmonellae (APHA, 2005).

Detection and enumeration of Staphylococcus sp. were carried out using membrane filter technique. A 100 ml drinking water samples were separately filtrated through the membrane filter (0.45 μm pore size and 47 mm diameter). The membrane was transferred onto Baird-Parker agar Base ((Himedia, India) for the selective isolation of coagulase-positive Staphylococcus aureus in water (APHA, 2005).  1ml of Nile water samples was inoculated into 5ml autoclaving buffer peptone water (British Standard Institute, 2002) tubes (incubated at 37ºC for 24 hours) which used as MPN technique. 0.2 ml from these tubes was streaked (by rod glass) on the plates of Baird-Parker agar medium. After incubation (37ºC for 24 hours), typical black colonies with or without metallic sheen and blackening extended beyond the colonies considered as confirmed positive results for the presence of Staphylococcus aureus (APHA, 2005).

Detection and enumeration of fungi and yeasts were using Saparoud agar medium and molt yeast extract medium respectively,   for raw water and drinking water according to APHA, 2005.

● Algae preparing

From Nile water Spirulina platensis was isolated and used in this study. The preparation and maintenance of the inoculums was accomplished using Zarrouk 's medium according to standard for the cultivation of this micro-alga. (Aly and Amber 2010).

Cladophora spp were collected in ice boxes (put into glass jars) from the beaches of River Nile in Port Said, area every week during May and November, 2010 and stored as mats at 10oC.

In this experiment were made two times every week (during May and November, 2010), Kg of both Cladophora sp. and Spirulina platensis (wet weight) was added to the lagoon of glass and passed  the raw Nile water with flow rate 2 liters / minute (figure 1).

Concentrations  A,B ; algal biomass ,and combined treatment  effect  of algal biomass and Cl2 concentrations  .A=6 ppm,B=2 ppm/

Results and Discussion :

Effect of Chorination on Nile water putification: Disinfection by chlorination can be problematic, in some circumstances. Chlorine can react with naturally occurring organic compounds found in the water supply to produce compounds known as disinfection byproducts (DBPs). The most common DBPs are trihalomethanes (THMs) and haloacetic acids (HAAs). Due to the potential carcinogenicity of these compounds, drinking water regulations across the developed world require regular monitoring of the concentration of these compounds in the distribution systems of municipal water systems. The World Health Organization has stated that the "Risks to health from DBPs are extremely small in comparison with inadequate disinfection."There are also other concerns regarding chlorine, including its volatile nature which causes it to disappear too quickly from the water system, and aesthetic concerns such as taste and odor. Chlorination is the process of adding the element chlorine to water as a method of water purification to make it fit for human consumption as drinking water. Water which has been treated with chlorine is effective in preventing the spread of waterborne disease. The chlorination of public drinking supplies was originally met with resistance, as people were concerned about the health effects of the practice. The use of chlorine has greatly reduced the prevalence of waterborne disease as it is effective against almost all bacteria and viruses, as well as amoeba.

Table 1. The log average counts for  classical bacterial indicators in Nile wate sitesr  with Cl2 sample .( the control).

| Site | Log number of cell forming unit (CFU) / 100 ml |
| --- | --- |
|  | Total viable bacterial count at:- | Bacterial indicators (MPN-index) |
|  | 37 oC | 22 oC | TC | FC | FS |
| Nile water | 7.1 | 6.6 | 4.8 | 3.6 | 2.8 |
| With Cl2a |  |  |  |  |  |
| 0 time | 6.8 | 6.1 | 4.2 | 3.2 | 2.4 |
| 10 minutes | 3.8 | 3.5 | 3.2 | 1.1 | 1.8 |
| 30 minutes | 1.8 | 1.1 | 1.1 | 0 | 1.1 |
| 60 minutes | 1.0 | 0.8 | 0 | 0 | 0.7 |
| 120 minutes | 0 | 0 | 0 | 0 | 0 |
| With Cl2b |  |  |  |  |  |
| 0 time | 6.6 | 6.4 | 4.2 | 3.2 | 3.6 |
| 10 minutes | 6.3 | 4.1 | 3.6 | 2.8 | 3.2 |
| 30 minutes | 3.9 | 3.8 | 2.4 | 1.7 | 2.8 |
| 60 minutes | 2.3 | 2.1 | 1.1 | 0.7 | 1.7 |
| 120 minutes | 1.1 | 0.7 | 0 | 0 | 0.6 |

Bromine in a concentration of 1·4 mg/l was injected for 9 hr; during eight consecutive nights into the Jordan channel. Chlorine and bromine were injected for the same time during two nights, to yield a total of 0·4 mg/1 residual. After 15 min contact, coliforms and fecal coli counts showed full correlation between disinfection capacity of bromine under these conditions to that achieved in the laboratory.Cosmarium, known to be resistant to chlorine, proved to be sensitive to bromine. Chroococcus found naturally in the water was shown to be sensitive to bromination. Chlorella, placed into the channel water in dialysing tubes, showed to react as in previous laboratory experiments.The combined use of chlorine and bromine in field experiment confirmed laboratory results in which higher algal and bacterial kill was achieved with mixtures of halogens than with any one of them separately.Table 2 indicated the gradual decrease in the pathogens  count in all microorganisms concerned with the two concentrations used with Cl2.

Table(2). The log average counts for pathogen counts  in Nile water after Cl2 treatment

| Treated sample | Log number of cell forming unit (CFU) / 100 ml |
| --- | --- |
|  | Salmonellae group | Pseudo.sp. | Total Staph | Total molds |
|  |  |  |  | yeast | fungi |
| Nile water | 7.1 | 6.6 | 4.8 | 3.6 | 2.8 |
| With Cl2a |  |  |  |  |  |
| 0 time | 1.8 | 2.6 | 2.4 | 2.9 | 3.4 |
| 10 minutes | 0 | 1.1 | 1.8 | 1.1 | 2.6 |
| 30 minutes | 0 | 0 | 1.4 | 0 | 1.8 |
| 60 minutes | 0 | 0 | 0 | 0 | 0.9 |
| 120 minutes | 0 | 0 | 0 | 0 | 0 |
| With Cl2b |  |  |  |  |  |
| 0 time | 2.4 | 2.4 | 2.1 | 2.7 | 3.2 |
| 10 minutes | 1.8 | 1.8 | 2.9 | 2.1 | 2.8 |
| 30 minutes | 0.7 | 0.7 | 0.7 | 1.4 | 1.8 |
| 60 minutes | 0 | 0 | 0.2 | 0.9 | 1.1 |
| 120 minutes | 0 | 0 | 0 | 0 | 0.3 |

Effect of Cladophora Algae on water purification

As it could be seen from table 3, either concentrations of the used Cl2 treatment resulted in decreasing the pathogens count especially with increasing the time of exposure .Cladophora aegagrophila is not really a plant, but a ball of algae, so it is a decorative exception from the rule about avoiding algae at all costs. It is normally found in shallow lakes, where the movement of the waves forms it into a sphere. In an aquarium it must be turned regularly to keep it in shape. Cladophora aegagrophila can be divided into smaller pieces, which become spherical with time, or which form a carpet, if attached to roots and stones. Associations between Cladophora and microbial communities are not well understood, although some research has presented evidence of a relationship between Cladophora and bacilliform bacteria (The cell wall of Cladophora provides a suitable attachment and grazing surface for many other organisms, such as diatoms, protozoa, mollusks, rotifers, and   young crayfish, and links between bacteria and algae have been found frequently in aquatic environments). Few  number of researches  findings the that  demonstrate the presence of fecal indicator bacteria, E. coli and enterococci, on Cladophora.

Table 3 indicated that Cladophora can be a secondary habitat for indicator bacteria that could potentially influence water quality. The long-term survival of E. coli and enterococci in Cladophora mats also has important ecological and public health implications. Masses of floating Cladophora, as a result of wave action, can release indicator bacteria and elevate their levels in the water. Also, algal mats washed onto beach sand may get buried in the sand by wave action or human activities, where they are protected from sunlight and desiccation. Here, indicator bacteria may multiply due to available nutrients from the decomposing mats; in turn, the beach sand can serve as a source of indicator bacteria for the nearshore water, especially when waves re-suspend buried mats. Previously, studies have shown that pathogenic bacteria (e.g., vibrios) are often associated with cladophora. It is possible that Cladophora provides a niche for pathogenic bacteria.

Combined effect of Cladophora and Cl2 on Nile  water purification:

Salmonella count is much more than other pathogens 7.1 compared to log CFU/100ml  6.6 and 4,8   for pseudcocci and staphilococci respectively. application of 6ppm Cl2 resulted in total disinfection ,however fungi still present with log. CFU/100ml 0.3after 120 min. Cladophora is a branching, green filamentous alga found naturally along the coastline of most of the Great Lakes There has been a recent resurgence of macroalgae, predominantly Cladophoral. These algae blooms lead to unsightly and foul-smelling beaches and have negative economic consequences as a result of the lowered beach use. In addition, Cladophora blooms result in reduced quality of drinking water and decreased property values. The offending plant is primarily Cladophora, a common filamentous green alga.? Growing on submerged rocks, it looks like long green hair waving in the water.? Cladophora is an important component of freshwater ecosystems, providing food and shelter for invertebrates and small fish.? The recent excessive blooms in the Great Lakes, however, signal an ecosystem responding to both natural changes and human impacts.

E. coli and enterococci survived for over 6 months in sun-dried and refrigerated Cladophora, perhaps other factors (competition, predation, and sunlight) were responsible for the gradual disappearance of E. coli and enterococci in naturally occurring Cladophora.While the case for natural multiplication needs further validation, Cladophora can be a reservoir for E. coli and enterococci. To understand the ecological and environmental implications of the present findings, more laboratory studies are necessary. These might include (i) in vitro studies showing the range of tolerance and growth potential of subject bacteria under a variety of environmental conditions (insolation, desiccation, and temperature), (ii) a thorough investigation of the genomic and phenotypic relationships of algae and ambient bacteria to investigate clonality or source-sink relationships further, (iii) noninvasive sterilization and inoculation of algae using wild and lab strains to discover intrinsic growth potential, maximum carrying capacity, and associated limiting factors, (iv) high-resolution microscopic studies of algal thalli and biofilm to further understand the physical association of algae and indicator bacteria, and (v) more investigations of the health implications of these findings. Our findings clearly suggest that Cladophora can be a secondary habitat for indicator bacteria that could potentially influence water quality in affected Great Lakes swimming areas. The long-term survival of E. coli and enterococci in Cladophora mats also has important ecological and public health implications. Masses of floating Cladophora, as a result of wave action, can release indicator bacteria and elevate their levels in the water.). As it could be seen from table 4, Cladophora macroalagae is more efficient in removing the pathogens especially when combined with Cl2.

Table( 3).Classical bacterial count on using Spirulina platensis and Cladophora.

| Site | Log number of cell forming unit (CFU) / 100 ml |
| --- | --- |
|  | Total viable bacterial count at:- | Bacterial indicators (MPN-index) |
|  | 37 oC | 22 oC | TC | FC | FS |
| Nile water | 7.1 | 6.6 | 4.8 | 3.6 | 2.8 |
| Algae 1 | 6.2 | 5.2 | 3.2 | 3.2 | 1.9 |
| Removal (%) | 12.7 | 21.1 | 33.3 | 11.1 | 32.1 |
| Algae1 Cl2a |  |  |  |  |  |
| 0 time | 5.5 | 4.9 | 2.8 | 2.4 | 1.4 |
| 10 minutes | 2.2 | 1.8 | 0.7 | 0 | 0.7 |
| 30 minutes | 1.1 | 0.6 | 0 | 0 | 0 |
| 60 minutes | 0 | 0 | 0 | 0 | 0 |
| 120 minutes | 0 | 0 | 0 | 0 | 0 |
| Algae 2 | 4.1 | 3.2 | 1.1 | 0.7 | 0.7 |
| Removal (%) | 42.3 | 51.5 | 77.1 | 80.6 | 75 |
| Algae2 Cl2b |  |  |  |  |  |
| 0 time | 3.9 | 2.9 | 0.7 | 0.7 | 0.7 |
| 10 minutes | 1.6 | 1.1 | 0 | 0 | 0 |
| 30 minutes | 0 | 0 | 0 | 0 | 0 |
| 60 minutes | 0 | 0 | 0 | 0 | 0 |
| 120 minutes | 0 | 0 | 0 | 0 | 0 |

FS: fecal streptococcus; FC fecal coliform; TC total colifom Aga 1 Cladophora Alga 2 Spirulina A Cl2 6ppm B 2ppm

Effect of Spirulina on Nile water purification:

Provide specifications for Spirulina, which include specifications for protein, lead, minerals, moisture, beta-carotene, total carotenoids, c-phycocyanin, arsenic, cadmium, mercury, pesticides, rodent hairs, and insect fragments. There also established the absence of E. coli, Salmonella, and Staphylococcus aureus, total aerobic bacteria of less than 200,000 colony forming units per gram (cfu/g), and total coliforms of less than 10 cfu/g. the composition of spirulina.   As an example of Spirulina powder used is  Pacifica™ which is  is a free-flowing green to bluish-green powder. It has a mild seaweed odor and is not soluble; it forms a suspension. The Particle size is <125 microns and Bulk Density is >0.48 (g/ml). Total aerobic bacteria: <105 cfu/gram
Total coliforms: <10 cfu/gramE. coli: negativePesticides: negative Arsenic: <0.5 ppm Cadmium: <0.2 ppm each Lead: <0.2ppm Mercury: <0.025 ppm Salmonella: negative

Combined effect of Spirulina  and Cl2 on Nile water purification:

The initial Spirulina inoculum concentrations used  (5x103 cells.mL) correspond to concentrations of around 0.1 g/L Lodi et al. (2003) studied the removal of nitrate and phosphorous from wastewater with S. platensis cultivation and concluded that biomass concentrations between 0.25 and 0.86 g/L result in larger removals of these pollutants. Therefore this microalgae can be an alternative to assist in the Nile water treatment, reducing the environmental impact caused by their pollutants and also to use the biomass produced in animal feed and fertilizers, in the production of pigments, vitamins, polysaccharides, including others treating with live Spirulina platensis decrease the pathogens to a removal % of 27.2 for samonella ,27.6 for Pseudococcus and 30.8 % for Staphellococci, 43.4% for yeasts and 33.3 % for fungi.On applying live Cladophora the ratio increased to 45.5, 62.1 and 92.3% for bathogen bacteria and 56.3 and 50%for fungi .

Table (4). the log average counts for pathogen counts  in nile water after cll2 treatment and algale

| Treated sample | Log number of cell forming unit (cfu) / 100 ml |
| --- | --- |
|  | Salmonellae group | Pseudo.sp | . Total staph. | Total molds |
|  |  |  |  | yeasts | fungi |
| Nile water | 2.2 | 2.9 | 2.6 | 3.2 | 3.6 |
| Algae1 | 1.6 | 2.1 | 1.8 | 2.1 | 2.4 |
| Removal% | 27.2 | 27.6 | 30.8 | 43.4 | 33.3 |
| Algae1+Cl2a |  |  |  |  |  |
| 0 time | 1.1 | 1.1 | 1.5 | 1.4 | 1.8 |
| 10 minutes | 0.2 | 0.4 | 0.6 | 0.7 | 1.1 |
| 30 minutes | 0 | 0 | 0 | 0 | 0 |
| 60 minutes | 0 | 0 | 0 | 0 | 0 |
| 120 minutes | 0 | 0 | 0 | 0 | 0 |
| Algae2 | 1.2 | 1.1 | 0.2 | 1.4 | 1.8 |
| Removal % | 45.5 | 62.1 | 92.3 | 56.3 | 50 |
| Algae2+Cl2b |  |  |  |  |  |
| 0 time | 0 | 0 | 0 | 0.4 | 0.6 |
| 10 minutes | 0 | 0 | 0 | 0 | 0 |
| 30 minutes | 0 | 0 | 0 | 0 | 0 |
| 60 minutes | 0 | 0 | 0 | 0 | 0 |
| 120 minutes | 0 | 0 | 0 | 0 | 0 |

Krebs & Sisler's method combines photosynthesis with photocatalysis to treat impure water and turn it into safe water, the company explaine the method involves water purification through a rapid growth in biomass, which also can be harvested and used for human or animal consumption, the treatment method is expected to produce potable water for half the cost of reverse osmosis  most commonly known to purify seawater as drinking water in large continuous-flow volumes while the biomass is produced and separated for consumption. the storehouse for atmospheric oxygen, carbon dioxide is the resource for recycling both oxygen and carbon. With the new process it can be separated through photosynthesis at a high rate. As the CO2 is separated the carbon grows biomass and the oxygen is released to enrich the air. The process is good for salt water, sewage and industrial wastewater, the company said. The biomass is produced by the concurrent use of photosynthesis and photocatalysis. Light emitting diode lighting and CO2 and balanced nutrients unite, growing a biomass from species of algae such as Spirulina.The biomass growth rate in deep well-lighted enclosed cells is expected to exceed 100 times the natural rate because all factors related to culturing the algae can be optimized in the continuous hydroponic process.

References:

- Desmarais, T. R., H. Solo-Gabriele, and C. J. Palmer.( 2002). Influence of soil on fecal indicator organisms in a tidally influenced subtropical environment. Appl. Environ. Microbiol. 68:1165-1172.

- Beaudeau, P., N. Tousset, F. Bruchon, A. Lefevre, and H. D. Taylor. (2001). In situ measurement and statistical modelling of Escherichia coli decay in small rivers. Water Res. 35:3168-3178.

- ALIBERT?, G.; OLGUIN, E. J.; de la NOUE, J. Mass cultivation and wastewater treatment using Spirulina. London: Taylor and Francis, 1997.

- LODI, A. et al. (2003). Nitrate and Phosphate renoval by Spirulina platensis. Journalof Industrial Microbiologyand Biotechnology, v. 30, n. 11, p. 656-660/

- RAMALHO, R. S. (1980) Treatment of residual waters. Barcelona: Revert.

- AMERICAN PUBLIC HEALTH ASSOCIATION - APHA. Standard methods for the examination of water and wastewater. 20 ed. Washington, (2000).

- Baker KH, Hegarty JP, Redmond B, Reed NA, Herson DS (2002). "Effect of oxidizing disinfectants (chlorine, monochloramine, and ozone) on Helicobacter pylori." (PDF). Applied and Environmental Microbiology 68 (2):981-984.

- .Shunji Nakagawara, Takeshi Goto, Masayuki Nara, Youichi Ozaqa, Kunimoto Hotta and Yoji Arata,( 1998). "Spectroscopic Characterization and the pH Dependence of Bactericidal Activity of the Aqueous Chlorine Solution", Analytical Sciences, 14, 69.

- Rose A. at al. (2006). "Solar disinfection of water for diarrhoeal prevention in Arch Dis Child 91 (2): 139-41. doi 16403847.

- Einarsson, A., Stefánsdóttir, G., Jóhannesson, H., Ólafsson, J.S., Gíslason, G.M. Wakana, I., Gudbergsson, G. and Gardarsson, A. (2004).The ecology of Lake Myvatn and the River Lax¨¢: variation in space and time. Aquatic Ecology 38:317-348.

- Hanyuda, T., Wakana, I., Arai, S., Miyaji, K., Watano, Y. and Ueda, K. (2002). Phylogenetic relationships within Cladophorales (Ulvophyceae, Chlorophyta) inferred from 18S rRNA gene sequences, with special reference to Aegagropila linnaei. J. Phycol. 38:564-71

- Chilton, E. W., R. L. Lowe, and K. M. Schurr. (1986). Invertebrate communities associated with Bangia atropurpurea and Cladophora glomerata in western Lake Erie. J. Great Lakes Res. 12:149-153.

- Taft, C. E. (1975). History of Cladophora in the Great Lakes, p. 5-16. In H. Shear and D. E. Konasewich (ed.), Cladophora in the Great Lakes. Great Lakes Research Advisory Board, International Joint Commission Regional Office, Windsor, Ontario, Canada.

- Rex, L. L., B. H. Rosen, and J. C. Kingston (1982). A comparison of epiphytes on Bangia atropurpurea (Rhodophyta) and Cladophora glomerata (Chlorophyta) from northern Lake Michigan. J. Great Lakes Res. 8:164-168.

- Richard L. Whitman, Dawn A. Shively, Heather Pawlik, Meredith B. Nevers, and Muruleedhara N. Byappanahalli(2003).Occurrence of Escherichia coli and Enterococci in Cladophora (Chlorophyta) in Nearshore Water and Beach Sand of Lake MichiganApplied and Environmental Microbiology, August, p.,. 69,(8): 4714-4719.

- Matsuo, Y., M. Suzuki, H. Kasai, Y. Shizuri, and S. Harayama. (2003). Isolation and phylogenetic characterization of bacteria capable of inducing differentiation in the green alga Monostroma oxyspermum. Environ. Microbiol. 5:25-35.

- Dick, L. K., Stelzer, E. A., Bertke, E. E., Fong, D. L., Stoeckel, D. M. (2010). Relative Decay of Bacteroidales Microbial Source Tracking Markers and Cultivated Escherichia coli in Freshwater Microcosms. Appl. Environ. Microbiol. 76: 3255-3262.

- Abdelzaher, A. M., Wright, M. E., Ortega, C., Solo-Gabriele, H. M., Miller, G., Elmir, S., Newman, X., Shih, P., Bonilla, J. A., Bonilla, T. D., Palmer, C. J., Scott, T., Lukasik, J., Harwood, V. J., McQuaig, S., Sinigalliano, C., Gidley, M., Plano, L. R. W., Zhu, X., Wang, J. D., Fleming, L. E. (2010). Presence of Pathogens and Indicator Microbes at a Non-Point Source Subtropical Recreational Marine Beach. Appl. Environ. Microbiol. 76: 724-732.

- Heaney, C. D., Sams, E., Wing, S., Marshall, S., Brenner, K., Dufour, A. P., Wade, T. J. (2009). Contact With Beach Sand Among Beachgoers and Risk of Illness. Am J Epidemiol 170: 164-172.

- Moriarty, E., Nourozi, F., Robson, B., Wood, D., Gilpin, B. (2008). Evidence for Growth of Enterococci in Municipal Oxidation Ponds, Obtained Using Antibiotic Resistance Analysis. Appl. Environ. Microbiol. 74: 7204-7210.

- Donovan, E. P., Staskal, D. F., Unice, K. M., Roberts, J. D., Haws, L. C., Finley, B. L., Harris, M. A. (2008). Risk of Gastrointestinal Disease Associated with Exposure to Pathogens in the Sediments of the Lower Passaic River. Appl. Environ. Microbiol. 74: 1004-1018.

- Shanks, O. C., Atikovic, E., Blackwood, A. D., Lu, J., Noble, R. T., Domingo, J. S., Seifring, S., Sivaganesan, M., Haugland, R. A. (2008). Quantitative PCR for Detection and Enumeration of Genetic Markers of Bovine Fecal Pollution. Appl. Environ. Microbiol. 74: 745-752

- Ksoll, W. B., Ishii, S., Sadowsky, M. J., Hicks, R. E. (2007). Presence and Sources of Fecal Coliform Bacteria in Epilithic Periphyton Communities of Lake Superior. Appl. Environ. Microbiol. 73: 3771-3778.

12/12/2010